There are 54 general-purpose I/O (GPIO) lines split into two banks. All GPIO pins have at
least two alternative functions within BCM. The alternate functions are usually peripheral IO
and a single peripheral may appear in each bank to allow flexibility on the choice of IO
voltage. Details of alternative functions are given in section 6.2. Alternative Function
Assignments.

The GPIO peripheral has three dedicated interrupt lines. These lines are triggered by the
setting of bits in the event detect status register. Each bank has its’ own interrupt line with the
third line shared between all bits.
The Alternate function table also has the pull state (pull-up/pull-down) which is applied after
a power down.

The GPIO has 41 registers. All accesses are assumed to be 32-bit
6.1 Register View

6.1 Register View continued

GPIO Function Select

******************************************
{Physical memory addresses of BCM2836 peripherals (See: BCM2835-ARM-Peripherals.pdf)}
 BCM2836_PERIPHERALS_BASE = $3F000000; {Mapped to VC address 7E000000}
 BCM2836_PERIPHERALS_SIZE = SIZE_16M;
 {Pin Output Set Registers}
 BCM2836_GPSET0 = $0000001C; {GPIO Pin Output Set 0}
 BCM2836_GPSET1 = $00000020; {GPIO Pin Output Set 1}

0x7E20 0000
 {GPIO (See Section 6)}
 BCM2836_GPIO_REGS_BASE = BCM2836_PERIPHERALS_BASE + $200000;
******************************************

GPIO Function Select

pin layout

# http://www.science.smith.edu/dftwiki/index.php/Tutorial:_Assembly_Language_with_the_Raspberry_Pi

as -o first.o first.s
gcc -o first first.o
# ./first | echo $?
# @ first.s
# @ from thinkingeek.com
# @ http://thinkingeek.com/2013/01/09/arm-assembler-raspberry-pi-chapter-1/
# @ Defines a main function that returns 2 as an exit code.
# @ as -o first.o first.s
# @ gcc -o first first.o
# @ ./first | echo $?
#
#
# .global main
#
# main: mov r0, #2 @ load immediate value 2 into Register r0
# bx lr @ return 2 to Operating Sytem
as -o hello.o hello.s
gcc -o hello hello.o
/hello

@ hello.s
@ D. Thiebaut
@ Just your regular Hello World program!
@
@ as -o hello.o hello.s
@ gcc -o hello hello.o
@ ./hello
@
@ Hello World!
@ ---------------------------------------
@ Data Section
@ ---------------------------------------

        .data
string: .asciz "\nHello World!\n"

@ ---------------------------------------
@ Code Section
@ ---------------------------------------

        .text
        .global main
        .extern printf

main:
        push {ip, lr}
ldr r0,=0x7e200000
mov r2,#1
str r2,r0
ldr r1,=0x7e20001c
        ldr r0, =string
        bl printf

        pop {ip, pc}

# Blinking LED

## C program

/* blink.c
   D. Thiebaut
   taken from https://www.raspberrypi.org/forums/viewtopic.php?f=33&t=23090
   blinks Physical Pin 7 On and Off, 10 times.

   to compile and run:
   gcc -o blink blink.c -lwiringPi
   sudo ./blink
*/

#include <wiringPi.h>
#include <stdio.h>
#include <stdlib.h>

int main ( void ) {
  int pin = 7;
  printf("Raspberry Pi wiringPi blink test\n");

  if (wiringPiSetup() == -1) {
    printf( "Setup didn't work... Aborting." );
    exit (1);
  }

  pinMode(pin, OUTPUT);

  int i;
  for ( i=0; i<10; i++ ) {
    digitalWrite(pin, 1);
    delay(250);

    digitalWrite(pin, 0);
    delay(250);
  }

  return 0;
}
## Assembly Version

as -o blink.o blink.s
gcc -o blink2 blink.o -lwiringPi
sudo ./blink2
@ blink.s
@ D. Thiebaut
@ based on the following C program:
@
@ #include <wiringPi.h>
@ #include <stdio.h>
@ #include <stdlib.h>
@
@ int main (void) {
@ int pin = 7;
@ printf("Raspberry Pi wiringPi blink test\n");
@
@ if (wiringPiSetup() == -1) {
@ printf( "Setup didn't work... Aborting." );
@ exit (1);
@ }
@
@ pinMode(pin, OUTPUT);
@ int i;
@ for ( i=0; i<10; i++ ) {
@ digitalWrite(pin, 1);
@ delay(250);
@
@ digitalWrite(pin, 0);
@ delay(250);
@ }
@
@ return 0;
@ }
@
@ To assemble, link, and run:
@
@ as -o blink.o blink.s
@ gcc -o blink2 blink.o -lwiringPi
@ sudo ./blink2

@ ---------------------------------------
@ Data Section
@ ---------------------------------------

        .data
        .balign 4
Intro: .asciz "Raspberry Pi wiringPi blink test\n"
ErrMsg: .asciz "Setup didn't work... Aborting...\n"
pin: .int 7
i: .int 0
delayMs: .int 250
OUTPUT = 1

@ ---------------------------------------
@ Code Section
@ ---------------------------------------

        .text
        .global main
        .extern printf
        .extern wiringPiSetup
        .extern delay
        .extern digitalWrite
        .extern pinMode

main: push {ip, lr} @ push return address + dummy register
        @ for alignment

@ printf( "blink..." ) ;
        ldr r0, =Intro
        bl printf

@ if (wiringPiSetup() == -1) {
@ printf( "Setup didn't work... Aborting." ) ;
@ exit (1) ;
@ }
        bl wiringPiSetup
        mov r1,#-1
        cmp r0, r1
        bne init
        ldr r0, =ErrMsg
        bl printf
        b done

@ pinMode(pin, OUTPUT) ;
init:
        ldr r0, =pin
        ldr r0, [r0]
        mov r1, #OUTPUT
        bl pinMode

@ for ( i=0; i<10; i++ ) {
        ldr r4, =i
        ldr r4, [r4]
        mov r5, #10
forLoop:
        cmp r4, r5
        bgt done

@ digitalWrite(pin, 1) ;
        ldr r0, =pin
        ldr r0, [r0]
        mov r1, #1
        bl digitalWrite

@ delay(250) ;
        ldr r0, =delayMs
        ldr r0, [r0]
        bl delay

@ digitalWrite(pin, 0) ;
        ldr r0, =pin
        ldr r0, [r0]
        mov r1, #0
        bl digitalWrite

@ delay(250) ;
        ldr r0, =delayMs
        ldr r0, [r0]
        bl delay

        add r4, #1
        b forLoop

done:
        pop {ip, pc} @ pop return address into pc